## Slide 1: Earth Orientation and GPS
Outline
Geodetic VLBI background
Applications of Geodetic VLBI
VLBI for Earth Orientation
Synergy with the VLBA
Dave Boboltz & Ken Johnston (USNO)

## Slide 2: VLBI Part of a Global Geodetic Observing System
Integrated Earth observing system
Space Geodetic Techniques
  VLBI, GPS, LLR, SLR, DORIS
  Global network of ground stations
Dedicated space missions
  Gravity Field, Altimetry, SAR, InSAR, Magnetic Field

## Slide 3: Geodetic VLBI and the IVS
Geodetic VLBI is coordinated through the International VLBI Service for Geodesy and Astrometry (IVS).
http://ivscc.gsfc.nasa.gov/

## Slide 4: Geodetic VLBI Data Path
Observations
  24-hr sessions 2+ times per week
  1-hr “intensive” sessions daily
Data transmission
  Mark5 modules shipped
  Electronic transmission (e-VLBI)
Correlation
  Mark 4 geodetic VLBI correlators
  DiFX software correlators
Post-processing
  Calibration, Fringe-fitting
  Experiment analysis

## Slide 5: Applications: Celestial Reference Frame
ICRF: quasi-inertial reference frame defined by VLBI estimates of the coordinates of 295 extragalactic radio sources
  Realization of International Celestial Reference System (ICRS)
  ICRF2 Adopted by the IAU January 1, 2010
The ICRF enables narrow-angle astrometry and precise spacecraft navigation
295 ICRF2 Defining Sources

## Slide 6: Applications: Terrestrial Reference Frame
ITRF: reference frame defined by estimates of the coordinates and velocities of a network of stations (VLBI, GPS, LLR, SLR, DORIS) on the surface of the Earth
Enables a wide range of geophysical science
  Structure and deformations of Earth’s crust, mantel & core
  Sea level change, earthquakes

## Slide 7: Applications: Earth Orientation
Earth Orientation Parameters (EOP) describe the orientation of the space axes of the Earth and provide the transformation between the CRF and the TRF
Include:
  Polar Motion (X-pole, Y-pole)
  Nutation (longitude Dy, obliquity De)
  Rotation rate (UT1-UTC)
Enable a variety of applications
  Transportation, geo-location, communications, navigation
Nutation
Polar Motion
Rotation Rate
(UT1-UTC)

## Slide 8: Earth Orientation at USNO
Analyzed VLBI results are distributed through the IVS
VLBI results combined with results from other techniques (i.e. GPS, SLR, LLR, DORIS)
Combined data then used to predict EOP into the future
Combination predictions are distributed through the IERS Rapid Service/Prediction Center for EOP at USNO
  IERS Bulletin A (finals.daily)
EOP results fed back to GPS
  Update GPS satellite orbit predictions
Accurate EOP predictions critical to various Govt. Agencies
  Future support for GPS III

## Slide 9: Combination of Space Geodetic Techniques
VLBI is only technique to uniquely determine
  The Celestial Reference Frame (ICRF)
  UT1 (Earth rotation angle relative to origin of ICRS)

## Slide 10: How Can UT1 Predictions be Improved?
Reducing data latency from 2.25 days to 6 hours results in:
  Factor of 5 reduction in UT1-UTC prediction uncertainty
  40% reduction UT1-UTC prediction errors 7 days out
Answer: e-VLBI

## Slide 11: Current e-VLBI Measurements of UT1
Daily 1-hr Intensive experiments coordinated through the IVS
  Int1 series Kokee Park, HI – Wettzell, Germany (Mon. – Fri.)
  Int2 series Tsukuba, Japan – Wettzell, Germany (Sat., Sun.)
Data transferred via e-VLBI to reduce latency
Correlated in Washington, Japan, or Bonn

## Slide 12: Synergy with the VLBA
USNO requirement to provide EOP to various Govt. Agencies
  Want US-controlled assets
  Plan for Continuity of Operations (COOP)
USNO and NASA-GSFC already collaborating with NRAO to maintain and improve the ICRF
  RDV experiments important part of ICRF2
  High-frequency (K/Q-band) reference frame observations
Could the VLBA provide a complimentary series of Intensive measurements for UT1?

## Slide 13: UT1 Testing With the VLBA
With in conjunction with NRAO, USNO began a series of “Pseudo-intensive” experiments to measure UT1
TC015
  5 stations (HN, LA, MK, PT, SC)
  13 experiments
  Optimized for MK-SC baseline
TB014
  3 stations (MK, LA, PT)
  5 experiments
  Optimized for MK-PT baseline

## Slide 14: Results from Pseudo-Intensive Experiments
  Shown are differences between VLBA UT1 measurements and IERS C04 combination solution as a function of baseline length
  Longer baselines more tightly distributed
  At the altitude of GPS constellation: 5ms ~ 1 cm
  Despite shorter baselines, VLBA measurements meet present and future requirements for UT1

## Slide 15: So Why Choose MK-PT Baseline?
Mauna Kea
  provides long east-west baseline necessary for UT1
  Infrastructure mostly there except for last mile
  Redundancy with Kokee Park geodetic VLBI station
Pie Town
  All fiber infrastructure already in place
  Cost sharing for some legs
  Proximity to NRAO-AOC

## Slide 16: USNO-NSF-NRAO MOU
USNO to make a significant contribution to VLBA operating costs beginning in 2012
In return USNO will receive:
  Access to MK - PT baseline for ~1.5 hr/day
    Single VLBA intensive experiment 7 days/week
    Back-up antenna (without e-VLBI) if needed
    Data to be streamed back to USNO via high-speed links
  Continued VLBA participation in the RDV experiments
    Six 24-hr experiments per year
    Vital to the CRF and TRF

## Slide 17: Current Status of the VLBA Intensive Program
Contracts in place to connect the Pie Town and Mauna Kea VLBA stations to high-speed networks in 2011
Contract with AUI/NRAO
  1 Gbps link from VLA to PT (Western NM Telecom)
  Access to shared 1 Gbps connections from the VLA to UNM
  Access to 10 Gbps NLR pop at UNM
  Equipment for both MK and PT
Contract with Univ. of Hawaii
  1 Gbps link from the MKOCN to the VLBA site
  Access to 10 Gbps Internet2 pop on Oahu back to mainland
  Subcontracted to Hawaiian Telecom
  Expect in-service: March 2011

## Slide 18: Pie Town to USNO Network Routing

## Slide 19: MKOCN Connectivity

## Slide 20: Summary
Geodetic VLBI is part of an integrated Earth observing system
Applications of Geodetic VLBI include: CRF, TRF, EOP
Earth Orientation vital to U.S. interests
VLBI is the only space geodetic technique that can provide CRF and UT1
VLBA is a useful asset for geodesy and increased interaction with the geodetic community (i.e. IVS, VLBI2010) is highly desirable
Geodetic VLBI is beneficial to astronomy:
  Correlator model inputs (TRF and EOP)
  Reference sources (CRF) for narrow-angle astrometry
  Observing techniques (DELZN troposphere)