## Slide 1: ALMA Observing Efficiency Drivers Correlator Workshop May 2016
Nick Whyborn
(nwhyborn@alma.cl)
ALMA Observatory System Engineer

## Slide 2
There is no direct requirement on the efficiency of concurrent observations using arrays, however…
  # 425 – Sub-array switching time < 3% relative to 300 s EB
  # 430 & 431 – Frequency tuning time < 1.5 s
  # 617 – Availability > 85% (goal 95%)
These all point to keeping overheads down at the few % level
The objective of the functional requirement for concurrent arrays is to allow efficient parallel observing, having activities on one array blocking observing on another clearly negates that objective.
Requirements

## Slide 3
The system requirements do not specify the allowed range of scan or sub-scan duration, the set-up time for the first in a sequence, or the dead-time between them in a sequence.
  What values of these key parameters are acceptable to users?
  Do we know the use-cases which dictate the needed extrema?
  What are the s/w & h/w tasks which constrain these parameters?
NB Only sub-scan duration etc appears to be relevant for the correlator
  Are the parameters for scan sequences important drivers elsewhere?
Perhaps an aside but…
  What are the defining characteristics of scans and sub-scans?
Limitations on sub-scan duration

## Slide 4
Proposal for sub-scan sequence limits
 | Actual | Desired
Minimum allowed duration (AtmCal, focus?) | 2 s | 2 s (ATM cal?)
Maximum allowed duration (lizajuous OTF map) | 20 mins ++ ? | >60 s
CORR set-up time for first sub-scan in a sequence | 5 s | 3.5 s + 2 dumps?
CORR dead-time between identical sub-scans in a sequence | 1.5 s ? | 0 s ?
CORR dead-time between different sub-scans in a sequence | 5 s ? | TDM: 2 TE FDM: 545 ms + ?
Time to release CORR resources at the end of a sequence | ? | <5 s ?
Ideally the configuration, read-out and clean-up activities on one array shall not affect read-out in other arrays
It is acceptable for configuration or clean-up activities on different arrays to execute consecutively rather than in parallel

## Slide 5
Corner cases mentioned
Raster mapping (blocker for astroholography)
  Map is executed as a sequence of ~100 sub-scans, each around 5 secs long
  It the solution to use a single continuous sub-scan?
Focus observations
  Several sequences each of one short sub-scan
ATM cal
  Sequence of 3 short sub-scans?

## Slide 6
Timing limitations of set-up tasks in station racks, correlator racks, LTA and elsewhere
Trade-off between long sub-scans versus multiple shorter sub-scans
  Does a new sub-scan only occur when the configuration changes?
Conflicts between configuring and running sub-arrays
  TFB scaling factors
  TFB LO frequency & phase set-up time
  LTA readout timing
Discussion areas