## Slide 1: SKA Band 3/4/5 feed package (and other related receiver work at Oxford)
Mike Jones
Jamie Leech, Angela Taylor, Bob Watkins, Amin Aminaei, Tommaso Ghigna, Alex Pollak, Jaz Hill-Valler, Lei Liu, John Saunders
University of Oxford
Andy Born
UKATC, Edinburgh
Wu Yang, Du Baio
JLRAT / CETC54, China

## Slide 2: SKA Mid feed packages
Band 1: 350 - 1050 MHz: Uncooled, QRFH (Chalmers – Miroslav Pantaleev et al)
Band 2: 950 – 1750 MHz: Cooled, ‘Corrugated’ (choked flange) 1.85:1 feed, 4-probe OMT (EMSS – Isak Theron et al)
Band 3/4/5(6) 1.65 – 24 GHz
Band 5a/b 4.6 – 15.4 (initially), Cooled single cryostat, up to five corrugated feeds.

## Slide 3: SKA Band 345 design brief
Band 5 at first light (4.6 – 13.8 GHz, originally 3:1 QRFH)
Bands 3, 4 (1.65 – 3.05, 2.8 – 5.2) to be retro-fittable
Option for a possible Band 6 (~15 – 24 GHz)
Shared vacuum manifold and He compressor with Band 2
Total cryogenics power budget for all bands < 5 kW
Concept: Single cryostat, single coldhead, multi-feeds

## Slide 4: Band 5 : QRFH vs dual CH
JLRAT QRFH and scaled EMSS Band 2 feeds: insert beam model in to GRASP SKA antenna model, integrate over 4p SKA sky/ground brightness model
Calculate FOM: (Aeff/Tsys)2
Decision: Dual feeds!
Band 5a: 4.6 – 8.5 GHz
Band 5b: 8.3 – 15.4 GHz (improved upper freq limit helps planet formation KSP)

## Slide 5: Bare horn pattern comparison
JLRAT QRFH
Chalmers Band B QRFH
Scaled EMSS corrugated horns:
Note: much higher beam circularity
Lower sidelobes
Much lower Cross-pol
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 6: Full optics beam comparison
JLRAT QRFH
Chalmers Band
B QRFH
Scaled EMSS corrugated horns:
Note: Much lower Cross-pol
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 7: Band 5 – Cross-polarization
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 8: Aperture efficiency
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 9: Tsys - Zenith
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 10: A/T - Zenith
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 11: Mapping Speed - Zenith
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 12
Mapping Speed – 60 degrees
Notes: SKA is in design phase – completing detailed design by 2017. 4 areas in Oxford: Software; SKA-LOW Digital signal processing and architecture; Dish receivers; Non-imaging processing (pulsars).
Software – at OERC. Areas as listed
Dishes – picture is a Gifford McMahon cold head! Aim is to reduce power consumption by a factor of a few for SKA1, order of magnitude for SKA2

## Slide 13: Cryostat concept
B3,4 – ambient feeds, cooled OMTs
B5a,b,6 – cooled (70 K) feeds, OMTs/LNAs @ 20 K
Single coldhead with plumbing

## Slide 14: First-light configuration

## Slide 15: SPF B345 on the Indexer

## Slide 16: SPF B345 on the Indexer

## Slide 17: Feeds and OMTs
B5a/b feeds from JLRAT, China
Feeds: Axial corrugated/choked flange (v. similar to B2)
B5a: Quad ridge
B5b: Turnstile

## Slide 18: Vacuum Window Design
Foam Support
Ring
Plastazote HD110
O-ring
O-ring
O-ring
Adapter Ring
Mylar Membrane
Mylar Clamping Ring
PTFE Membrane
PTFE Clamping Ring
Vacuum Flange
WINDOW COMPONENTS FITTED TO CRYOSTAT DEVELOPMENT CHAMBER

## Slide 19: Prototype Window (B5a)
Vacuum seal is Mylar
Supported by Plastazote (polythene/N2)
Modest infra-red block (single layer) – reduces heat load x 2.
Outer PTFE weather cover.

## Slide 20: Feed Unit

## Slide 21: Feed Unit

## Slide 22: Feed unit - exploded

## Slide 23: LNAs and RF chain

## Slide 24: LNAs and RF chain
Very simple RF chain: LNA, filter, 2nd stage amp
1-20 GHz warm amplifiers
Custom BPFs

## Slide 25: Cold plumbing

## Slide 26: Cold plumbing

## Slide 27: Cryogenics – cold head
Oxford Cryosystems Coolstar 2/9 and 6/30 – both variable speed (stepper motor ~20 – 90 rpm)
Initial design was 2/9 (same as MeerKAT, Band 2) – close to estimated head load.
Now baseline is 6/30 – option to run slow (20 – 90 rpm). Higher heat lift for initial cooldown, reduced wear in steady-state.
Even at full speed, within power budget (5 kW) – can run a 2/9 (Band 2) and 6/30 (B5) < 3 kW

## Slide 28: Cryogenics – power control
Horrible multi-dimensional problem, but:
Best heat lift at high pressures, low coldhead speeds
Heat lift saturates or even declines at very high coldhead speeds
Power consumption declines linearly with compressor speed
Conclusion: control of both coldhead and compressor speed allows you to optimize power consumption for any required heat lift

## Slide 29: Cryogenics – power control

## Slide 30: Cryogenics - compressor
Need variable flow compressor to ensure no wasted compressed He
Oxford Cryosystems developed new SKA-optimized compressor:
  Hitachi 3 kW 3-ph scroll compressor capsule
  EMSS MeerKAT RFI-tight control/monitoring module
  External variable-speed 3-ph x 240V variable freq drive
  Rugged housing for outdoor use
  Zero-maintenance air-cooled heat exchanger
  ~30,000h adsorber lifetime

## Slide 31: Goonhilly-3 4-8.5 GHz receiver
C/X band receiver for eMerlin,single-dish and satcoms
Compact 2.2:1 OMT
CW stabilized for total power observations

## Slide 32: CW stabilization
Total power observations need suppression of 1/f noise
Continuous-comparison architecture (e.g. Planck LFI, C-BASS) needs 4xRF channels
Noise stabilization takes up sensitivity
CW stabilization takes up small fraction of bandwidth, can use strong cal signal
Measurements show 1/f fluctuations highly correlated across band

## Slide 33: AVN demonstration Rx
PhD project to build demonstration Rx covering SKA Band 5 with new technology:
Wide-band tri-ridge-transducer
Flared corrugated horn
RFSOC-based digital backend with arbitrary calibration signal generation

## Slide 34: Feed horn design
Chokes: lower sidelobes
Smooth wall: Mode conversion and impedance matching
Corrugated wall: ensures TE11 & TM11 (HE11) propagates to aperture
TE11
TM11
HE11
+
TE: Transverse Electric Field
TM: Transverse Magnetic Field
TE11
Linear polarised
Cross section of Feed Horn Design
[5]

## Slide 35: Feed horn design
11dB
-25dB
Gain:
-12dB
HFSS Horn Simulation Results
CHAMP Horn Simulation: Beam Pattern
≈ -15dB at 58º half beamwidth
4.6 to 8.5 GHz
15dB polarisation isolation minimum
Beam Pattern measurement yet to be carried out

## Slide 36: Transducer Design
For wideband operation Quad ridge Othormode transducer is widely used
  Provides wide band operation
  Imperfect Manufacturing process produce asymmetries resulting in spurious mode generation
   loss off sensitivity at the wavelengths this occurs
   Coupling between polarisations
Triple ridge structures have been known to provide wider bandwidth capabilities [7], But has not to date been implemented.
Desired TE11
Unwanted TE21
TE: Transverse Electric Field
OMT: Orthomode Transducer
QROMT
Proposed TRT
[6]
TRT: Triple Ridge Transducer

## Slide 37: Transducer Design
Ridge profile of the form C+A*sin(B)2
Waveguide Diameter reduces at Coaxial transition end
 Improves high freq. performance
Approx. 320mm total length
Transducer Solid Model

## Slide 38: Transducer Design
X and Y polarisation couple linearly into all 3 Coaxial ports as expected
Return Loss better than -20 dB over desired band (4.6 to 8.5 GHz)
Potential for 3.47:1 -15 dB bandwidth operation
Transducer HFSS S-parameter Simulation Results

## Slide 39: Transducer Design
HFSS Transducer Simulation Results
Verified that power excited at the waveguide port is transmitted into the coaxial ports

## Slide 40: Noise injection

## Slide 41: RECEIVER BLOCK DIAGRAM
Preliminary design likely to change to allow for greater bandwidth provided by the transducer
DAC

## Slide 42: Conclusions
SKA is a multi-feed package design, one ambient, two cooled
SKA Band 3/4/5 is currently implementing a multi-feed cryostat, optimized for A/T on the SKA optics, with reduced cryogenic power consumption from a single variable-speed compressor feeding variable-speed coldheads.
Prototype bench tests Mar 2019
SKA designs are basically frozen, but interesting new technologies also being studied.