## Slide 1: Conical Corrugated Horns - Design & Performance
Sivasankaran Srikanth NRAO, Charlottesville, VA
Caltech ngVLA Optics Workshop
Pasadena, CA, June 19-20, 2018

## Slide 2
CONTENTS
LINEAR TAPER HORNS – NARROW FLARE ANGLE
PROFILE/COMPACT HORNS
LINEAR TAPER HORNS– WIDE FLARE ANGLE

## Slide 3
WHY CORRUGATED HORNS?
FOCAL PLANE FIELDS AND APERTURE FIELDS
SYMMETRIC E- AND H-PLANE PATTERNS
NEARLY CONSTANT BEAM WIDTH
LOW CROSSPOLARIZATION
GOOD INPUT MATCH
WIDE BANDWIDTH
LOW LOSS
WELL DEFINED PHASE CENTER
TM1n
TE1n
HE1n

## Slide 4
LINEAR TAPER CORRUGATED HORN – NARROW FLARE ANGLE
FEED | Freq (GHz) | Taper (dB) @θsub | θf | DIA ” | DIA/λ * | Δ | L/λ * | Taper **
EVLA-Ku | 12-18 | -14@9.25° | 10.38° | 12.33 | 12.5 | 0.574 | 32.3 | -14.0
SHAO-Ku | 12-18 | -15.5@13º | 13.3º | 8.53 | 8.7 | 0.505 | 17.3 | -15.6
VLBA-Ku | 12-15.4 | -14@13.25° | 14° | 8.00 | 8.1 | 0.500 | 14.7 | -14.5
GBT-Ku | 12-18 | -13@15º | 17.5º | 8.33 | 8.5 | 0.652 | 13.1 | -13.4
θf
DIA
L
* λ at low end
** Measured (dB)
Aperture phase error factor
Δtan

## Slide 5
HALF BEAM WIDTH at -3, -10, -20 dB Vs D/λ
b
EVLA Ku (9.3º)
SHAO Ku (13º)
VLBA Ku (13.3º)
GBT Ku (15º)
12.5λ
8.7λ
8.5λ
8.1λ
θf
D/λ
17.5⁰
14⁰
13.3⁰
10.4⁰
P. J. B. Clarricoats and A. D. Olver “Corrugated horns
For microwave antennas” Peter Peregrinus Ltd. , London, UK
θsub

## Slide 6
CONVENTIONAL & RING-LOADED CORRUGATIONS
Y. Takeichi, T. Hashimoto and F. Takeda, “The ring-loaded corrugated waveguide,” IEEE Trans. MTT
Vol. MTT-19, pp. 947-950, Dec. 1971.
F. Takeda and T. Hashimoto, “Broadbanding of corrugated conical horns by means of the ring-loaded
Corrugated structure,” IEEE Trans. Antennas & Propagat., vol AP-24, pp. 786-792, Nov. 1976.
0.5lh
0.2ll
0.45lh
0.2ll
flow
fhigh

## Slide 7
LINEAR TAPER HORN; NARROW FLARE ANGLE
GBT Ku (12-18 GHz)
8.33”
Δ=0.65l
17.5º
12.86”

## Slide 8
MEASURED BEAM PATTERNS E-, H-PLANES
Chart: 12 - 18 GHz FEED HORN; H-plane
Chart: 12-18 GHz FEED HORN; E-plane
Freq. (GHz) | E-plane @15⁰ | H-plane @15⁰ | Average
10.6 | -12.6 | -12.0 | -12.2
11.0 | -13.0 | -12.2 | -12.4
12.0 | -13.3 | -13.0 | -13.1
13.0 | -14.6 | -14.1 | -14.3
15.0 | -13.0 | -13.3 | -13.1
16.0 | -14.1 | -14.1 | -14.1
18.0 | -12.1 | -12.7 | -12.4

## Slide 9
PHASE PATTERNS , PHASE CENTER LOCATION
Chart: E-plane
Chart: H-plane
Frequency (GHz) | PC from aperture (ins)
12 | -10.2
15 | -12.0
18 | -13.0
PC travel =3.56lmid
=0.14L

## Slide 10
CROSS-POLAR PATTERNS IN 45º-PLANE
Chart: D-plane; Crosspolarization
Chart: D-plane; Crosspolarization

## Slide 11
Chart: 18.0 GHz; H-plane
SIMULATION AND MEASUREMENT
Chart: 18.0 GHz; E-plane
Chart: 15.0 GHz; E-plane
Chart: 11.0 GHz; E-plane
Chart: 11.0 GHz; H-plane
Chart: 15.0 GHz; H-plane

## Slide 12
MEASURED PATTERNS E-, H-PLANES
Chart: 12.0 GHz
Chart: 15.0 GHz
Chart: 18.0 GHz
Chart: 10.6 GHz
Chart: 19.0 GHz

## Slide 13
MEASURED INPUT MATCH
Chart: Return Loss; 11-18 GHz Feed ; with radome
MEASFEED>GBTKuWide>Feed>GBTKuJULY262012>VSWR>Feed

## Slide 14
APERTURE EFFICIENCY, TSYSTEM ON THE GBT (4-8 GHz)
Chart: GBT C- Band
| 4 | 5 | 6 | 7 | 8
Ap. Eff | 61.7 | 70 | 72.5 | 69 | 66.3
Chart: GBT C- Band
| 4 | 5 | 6 | 7 | 8
Tsys | 20 | 17.7 | 20 | 23 | 33
Trx | 15 | 9 | 10 | 13 | 14
“The Proposer’s Guide for the Green Bank Telescope”,
GBT Support Staff, January 5, 2015
-15dB @15⁰
D=25.9” (8.8l)
L=43.3” (14.7l)
Θf=16.4⁰
Δ=0.63l

## Slide 15
PROFILE TAPER (COMPACT) CORRUGATED HORN
FEED15.0 | Freq (GHz) | Taper (dB) @ θsub | θmax | DIA” | DIA/λ * | L/λ * | Taper (dB)**
EVLA-C | 4-8 | -13@9.25° | 12.0° | 22.12 | 7.5 | 21.1 | -12.5
VLBA-C | 4-8 | -14@13.25° | 15.0° | 13.78 | 4.7 | 10.6 | -13.7
GBT-K | 18-26.5 | -13@15º | 17.0º | 2.93 | 4.5 | 8.6 | -13.3
DIA
θmax
L
Diameter 35% smaller
Length 25% less
*λ at low end
** Measured (dB)

## Slide 16
PROFILE/COMPACT HORN VLBA (4-8 GHz)
-14dB @ 13.3º
Aperture dia 13.8”(4.7l); Length 31.4”(10.6l); θstart =8°; θmax=15°
8 ring-loaded corrugations; Total 68 corrugations
PROFILE HORNS
GBT: L, S
EVLA: L, S, C
VLABA: L, C

## Slide 17
MEASURED BEAM PATTERNS E-, H-PLANES
Chart: E-Plane
Chart: H-Plane
Freq. (GHz) | E-plane @13.3⁰ | H-plane @13.3⁰ | Average
4.0 | -9.6 | -10.6 | -10.1
4.3 | -11.6 | -12.1 | -11.9
5.0 | -14.7 | -13.7 | -14.2
5.7 | -14.0 | -13.5 | -13.8
6.0 | -13.9 | -13.3 | -13.6
6.7 | -13.6 | -14.1 | -13.8
7.0 | -14.4 | -14.5 | -14.4
7.3 | -15.3 | -15.2 | -15.3
7.7 | -14.6 | -16.5 | -15.5
8.0 |  | -16.2 | -16.2

## Slide 18: PHASE PATTERNS AND PHASE CENTER LOCATION
Chart: E-Plane
Chart: H-Plane
Frequency (GHz) | PC from aperture (ins)
4.0 | -9.4
5.0 | -17.6
6.0 | -21.2
7.0 | -25.3
7.7 | -29.5
8.0 | *
PC travel =10.2lmid
=0.64L

## Slide 19
CROSS-POLAR PATTERNS IN THE 45º-PLANE
Chart: 45°-Plane; Crosspolarization
Theory -24dB

## Slide 20
SIMULATION AND MEASUREMENT
Chart: E-Plane at 4.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -22.1476 | -21.294 | -20.6491 | -20.1992 | -19.9335 | -19.8368 | -19.8773 | -19.9844 | -20.0166 | -19.7521 | -18.9779 | -17.663 | -15.987 | -14.1776 | -12.3908 | -10.7043 | -9.1482 | -7.7985 | -6.4946 | -5.3245 | -4.2824 | -3.3629 | -2.5613 | -1.8735 | -1.2963 | -0.8272 | -0.4643 | -0.206 | -0.0515 | 0 | -0.0515 | -0.206 | -0.4643 | -0.8272 | -1.2963 | -1.8735 | -2.5613 | -3.3629 | -4.2824 | -5.3245 | -6.4946 | -7.7985 | -9.1482 | -10.7043 | -12.3908 | -14.1776 | -15.987 | -17.663 | -18.9779 | -19.7521 | -20.0166 | -19.9844 | -19.8773 | -19.8368 | -19.9335 | -20.1992 | -20.6491 | -21.294 | -22.1476
Meas | -22.007 | -20.966 | -20.395 | -19.928 | -19.562 | -19.605 | -19.828 | -20.276 | -20.945 | -21.07 | -20.429 | -18.918 | -16.547 | -14.484 | -12.299 | -10.52 | -8.97 | -7.352 | -6.171 | -4.895 | -3.992 | -3.061 | -2.454 | -1.825 | -1.16 | -0.852 | -0.406 | -0.074 | 0 | 0.1 | -0.113 | -0.26 | -0.55 | -0.94 | -1.416 | -1.88 | -2.732 | -3.403 | -4.276 | -5.39 | -6.4 | -7.865 | -9.339 | -11.072 | -12.781 | -15.055 | -17.264 | -19.422 | -20.823 | -21.225 | -20.844 | -20.163 | -19.779 | -19.565 | -19.816 | -20.05 | -20.548 | -21.528 | -22.623
Chart: H-Plane at 4.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -25.7475 | -23.834 | -22.3068 | -21.0972 | -20.1628 | -19.4751 | -19.0104 | -18.7388 | -18.6075 | -18.5157 | -18.2897 | -17.711 | -16.6429 | -15.1494 | -13.4302 | -11.6727 | -9.9904 | -8.4213 | -6.9833 | -5.6986 | -4.5623 | -3.5673 | -2.7063 | -1.9727 | -1.3609 | -0.8664 | -0.4853 | -0.2151 | -0.0537 | 0 | -0.0537 | -0.2151 | -0.4853 | -0.8664 | -1.3609 | -1.9727 | -2.7063 | -3.5673 | -4.5623 | -5.6986 | -6.9833 | -8.4213 | -9.9904 | -11.6727 | -13.4302 | -15.1494 | -16.6429 | -17.711 | -18.2897 | -18.5157 | -18.6075 | -18.7388 | -19.0104 | -19.4751 | -20.1628 | -21.0972 | -22.3068 | -23.834 | -25.7475
Meas | -25.33 | -23.52 | -21.985 | -20.908 | -20.078 | -19.419 | -18.967 | -18.796 | -18.555 | -18.619 | -18.256 | -17.749 | -16.681 | -15.109 | -13.434 | -11.545 | -9.906 | -8.274 | -6.851 | -5.722 | -4.428 | -3.662 | -2.722 | -2.085 | -1.303 | -0.943 | -0.412 | -0.095 | 0 | 0.021 | -0.077 | -0.382 | -0.525 | -1.013 | -1.63 | -2.194 | -2.948 | -3.827 | -4.813 | -6.015 | -7.349 | -8.835 | -10.483 | -12.146 | -13.855 | -15.43 | -16.858 | -17.743 | -18.195 | -18.552 | -18.518 | -18.793 | -19.071 | -19.391 | -20.188 | -21.158 | -22.241 | -23.737 | -25.699
Chart: E-Plane at 6.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -34.2868 | -30.8686 | -28.6336 | -27.2555 | -26.6091 | -26.658 | -27.3524 | -28.2901 | -28.0108 | -25.555 | -22.4367 | -19.7077 | -17.5402 | -15.8847 | -14.6613 | -13.7808 | -13.1229 | -12.5091 | -11.7118 | -10.5578 | -9.0598 | -7.4019 | -5.7512 | -4.2454 | -2.9471 | -1.8814 | -1.055 | -0.4677 | -0.1167 | 0 | -0.1167 | -0.4677 | -1.055 | -1.8814 | -2.9471 | -4.2454 | -5.7512 | -7.4019 | -9.0598 | -10.5578 | -11.7118 | -12.5091 | -13.1229 | -13.7808 | -14.6613 | -15.8847 | -17.5402 | -19.7077 | -22.4367 | -25.555 | -28.0108 | -28.2901 | -27.3524 | -26.658 | -26.6091 | -27.2555 | -28.6336 | -30.8686 | -34.2868
Meas | -36.511 | -32.196 | -29.419 | -27.649 | -26.55 | -26.48 | -27.316 | -28.94 | -29.974 | -27.588 | -23.923 | -20.859 | -18.298 | -16.308 | -15.039 | -14.261 | -13.446 | -12.958 | -12.118 | -10.895 | -9.354 | -7.504 | -5.652 | -4.224 | -2.914 | -1.855 | -1.016 | -0.372 | 0 | -0.079 | -0.336 | -0.757 | -1.401 | -2.432 | -3.531 | -5.218 | -6.695 | -8.539 | -10.409 | -11.725 | -12.607 | -13.379 | -13.949 | -14.746 | -15.716 | -17.358 | -19.614 | -22.418 | -25.918 | -29.349 | -29.73 | -28.143 | -26.877 | -26.535 | -27.057 | -28.482 | -30.35 | -33.52 | -38.653
Chart: H-Plane at 6.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -35.2801 | -31.1791 | -28.5536 | -26.901 | -26.0362 | -25.9092 | -26.5203 | -27.7022 | -28.2893 | -26.3392 | -23.0158 | -19.9889 | -17.5866 | -15.756 | -14.4031 | -13.4344 | -12.738 | -12.1524 | -11.4577 | -10.4482 | -9.0744 | -7.4724 | -5.8344 | -4.3179 | -3.0011 | -1.9168 | -1.0751 | -0.4765 | -0.1189 | 0 | -0.1189 | -0.4765 | -1.0751 | -1.9168 | -3.0011 | -4.3179 | -5.8344 | -7.4724 | -9.0744 | -10.4482 | -11.4577 | -12.1524 | -12.738 | -13.4344 | -14.4031 | -15.756 | -17.5866 | -19.9889 | -23.0158 | -26.3392 | -28.2893 | -27.7022 | -26.5203 | -25.9092 | -26.0362 | -26.901 | -28.5536 | -31.1791 | -35.2801
Meas | -38.33 | -32.822 | -29.535 | -27.463 | -26.395 | -25.958 | -26.163 | -27.307 | -28.043 | -26.996 | -23.63 | -20.636 | -18.094 | -16.135 | -14.536 | -13.574 | -12.857 | -12.024 | -11.313 | -10.263 | -8.865 | -7.306 | -5.606 | -4.092 | -2.847 | -1.791 | -0.955 | -0.266 | 0 | 0.128 | -0.22 | -0.644 | -1.422 | -2.31 | -3.558 | -4.935 | -6.485 | -8.228 | -9.851 | -10.928 | -11.896 | -12.619 | -13.232 | -14.145 | -15.567 | -17.291 | -19.406 | -22.287 | -25.485 | -27.85 | -27.86 | -26.624 | -26.096 | -26.233 | -26.795 | -28.278 | -30.551 | -34.222
Chart: E-Plane at 8.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -46.201 | -37.7681 | -32.1538 | -29.2022 | -27.9068 | -28.033 | -29.5204 | -30.851 | -27.9754 | -23.8607 | -20.8628 | -18.9709 | -17.9392 | -17.4261 | -16.8003 | -15.3512 | -13.1651 | -10.9149 | -9.019 | -7.5833 | -6.5643 | -5.8372 | -5.2133 | -4.4967 | -3.5733 | -2.5206 | -1.5097 | -0.6963 | -0.1774 | 0 | -0.1774 | -0.6963 | -1.5097 | -2.5206 | -3.5733 | -4.4967 | -5.2133 | -5.8372 | -6.5643 | -7.5833 | -9.019 | -10.9149 | -13.1651 | -15.3512 | -16.8003 | -17.4261 | -17.9392 | -18.9709 | -20.8628 | -23.8607 | -27.9754 | -30.851 | -29.5204 | -28.033 | -27.9068 | -29.2022 | -32.1538 | -37.7681 | -46.201
Meas | -50.885 | -57.305 | -43.679 | -39.407 | -37.347 | -38.348 | -41.516 | -52.816 | -40.267 | -34.042 | -31.073 | -29.882 | -30.209 | -29.779 | -26.29 | -22.073 | -18.612 | -15.921 | -13.842 | -12.426 | -10.977 | -9.277 | -7.366 | -5.563 | -3.707 | -2.264 | -1.293 | -0.439 | 0 | -0.027 | -0.286 | -0.903 | -1.867 | -3.283 | -4.748 | -6.75 | -8.563 | -10.165 | -11.792 | -13.122 | -14.773 | -17.236 | -20.513 | -24.67 | -28.71 | -30.52 | -29.696 | -30.203 | -32.809 | -37.045 | -49.408 | -44.58 | -39.172 | -37.811 | -38.861 | -41.049 | -45.593 | -63.793 | -48.111
Chart: H-Plane at 8.0 GHz
| -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Theo | -46.4457 | -36.2778 | -31.5939 | -29.236 | -28.4856 | -29.3267 | -32.1015 | -34.278 | -29.1947 | -24.602 | -21.7878 | -20.3043 | -19.8963 | -20.2392 | -20.249 | -18.3601 | -15.3537 | -12.6522 | -10.6383 | -9.2842 | -8.4551 | -7.9215 | -7.3264 | -6.3212 | -4.8819 | -3.3125 | -1.9174 | -0.8633 | -0.217 | 0 | -0.217 | -0.8633 | -1.9174 | -3.3125 | -4.8819 | -6.3212 | -7.3264 | -7.9215 | -8.4551 | -9.2842 | -10.6383 | -12.6522 | -15.3537 | -18.3601 | -20.249 | -20.2392 | -19.8963 | -20.3043 | -21.7878 | -24.602 | -29.1947 | -34.278 | -32.1015 | -29.3267 | -28.4856 | -29.236 | -31.5939 | -36.2778 | -46.4457
Meas | -44.302 | -43.033 | -35.391 | -31.546 | -29.782 | -29.281 | -30.557 | -33.05 | -31.454 | -26.41 | -22.912 | -20.855 | -19.702 | -19.253 | -18.918 | -17.633 | -15.057 | -12.283 | -10.055 | -8.551 | -7.306 | -6.393 | -5.508 | -4.458 | -3.229 | -2.13 | -1.26 | -0.345 | 0 | 0.162 | -0.213 | -0.885 | -1.654 | -2.722 | -3.988 | -5.108 | -5.978 | -6.915 | -7.91 | -9.396 | -11.13 | -13.653 | -16.534 | -18.463 | -19.046 | -19.378 | -20.328 | -21.917 | -24.441 | -28.805 | -33.261 | -31.942 | -29.629 | -29.312 | -30.609 | -33.609 | -39.374 | -49.737 | -41.137

## Slide 21
MEASURED PATTERNS E-, H-PLANE
Chart: E & H planes at 4.0 GHz
Chart: E & H planes at 6.0 GHz
Chart: E & H planes at 7.7 GHz
Chart: E & H planes at 8.0 GHz

## Slide 22
MEASURED INPUT MATCH
Chart: VLBA; C-band Feeds #1, 2

## Slide 23
APERTURE EFFICIENCY, TSPILLOVER ON EVLA (4-8 GHz) ANTENNA # 13
Chart: EVLA C- Band
| 4 | 4.8499999999999996 | 5 | 6.024 | 7.048 | 8
Ap. Eff | 55 | 55 | 54 | 67 | 62 | 64
EVLA Memo 90, “Performance Tests of the EVLA C-Band Feed”,
R. Perley and R. Hayward, February 16, 2005
4.5K Tspill @ 60º
= 93 to 95%
-13dB @9.25⁰

## Slide 24
LINEAR TAPER HORN; WIDE FLARE ANGLE
12.-2.4 GHz
Taper -13 dB at 46⁰
λ-wavelength at 1.2 GHz
Dia=554mm (2.2λ)
Length=187mm(0.8λ)
Θf=45⁰
Δ=0.46l
# corrg. 8
46º
179mm
Slot depth
#1=53.7mm (0.21λ)
#8=48.8mm (0.19λ)
R. Lehmensiek, D.L. de Villiers, “Wide Flare Angle Axially Corrugated Conical Horn Design for a Classical Offset Dual-Reflector Antenna”, 6th EUCAP
4.4λ
2.2λ

## Slide 25
SIMULATIONS E-, H-, XPOL, S11
Chart: 45 Degree Horn; H-Plane
Chart: 45 Degree Horn; E-Plane
Chart: 45 Degree Horn; D-Plane
@46⁰
-14.3
-22.5
@46⁰
-14.2
-16.3
-35dB

## Slide 26
SIMULATIONS E- & H- PLANES
Chart: 45 Degree Horn; 1.8 GHz
Chart: 45 Degree Horn; 2.4 GHz
Chart: 45 Degree Horn; 1.2 GHz

## Slide 27
GREGORIAN ANTENNA Θsub 15º, 18º
Sub 3.2x3.351; θs=15º
f=4.6285
Sub 3.2x3.340; θs=18º
f=3.5870
15º
18º

## Slide 28
GREGORIAN ANTENNA Θsub 46º, 55º
Sub 3.2x3.398; θs=46º
f=1.2595
Sub 3.2x3.439; θs=55º
f=1.2290
46º
55º

## Slide 29
1.2 to 2.4 GHz FEED HORNS FOR θsub = 15º, 18º, 46º
Frequency 1.2-2.4 GHz
Taper -13 dB
λ-wavelength at 1.2 GHz
Dia=1150mm (4.6λ)
Length=2160mm(8.6λ)
Θmax=18.5⁰
# corrg. 83
Dia=963mm (3.9λ)
Length=1457mm(5.8λ)
Θmax=22⁰
# corrg. 56
Dia=554mm (2.2λ)
Length=187mm(0.8λ)
Θf=45⁰
# corrg. 8
15º
18º
46º
Dia=2115mm (8.5λ)
Length=2979mm(11.9λ)
Θf=17.8⁰
# corrg. 88
15º

## Slide 30
PHASE CENTER LOCATION
Profile Horn (4.6λ)
Length=2160mm
Profile Horn (3.9λ)
Length=1457mm
Axial Corrg. Horn (2.2λ)
Length=187mm
ΔPC = 1500mm
(9λmid)
ΔPC = 1050mm
(6.3λmid)
ΔPC = 100mm
(0.6λmid)
Eco – E plane
Eco - 45 degree
Eco – H plane
-1925
-1310
-215
15º
15º
46º
18º
Lin. Horn (8.5λ)
Length=2979mm
ΔPC = 700mm
(4.2λmid)
-3150

## Slide 31
Half Beam Width at -15 dB
Profile Horn (4.6λ)
Length=2160mm
Axial Corrg. Horn (2.2λ)
Length=187mm
Eco :E-plane
Eco : 45 degree
Eco : H-plane
15º
46º
15º
Profile Horn (3.9λ)
Length=1457mm
18º
Lin. Horn (8.5λ)
Length=2979mm

## Slide 32
ANTENNA BEAM AT 1.2 GHz
Θsub=15º
44.91 dB
Xpol -37.1 dB
Θsub=15º
45.75 dB
Xpol -36.7 dB
Θsub=18º
44.84 dB
Xpol -34.9 dB
Θsub=46º
45.10 dB
Xpol -34.1 dB
Eco, Ecx -Symmetric
Eco, Ecx - 45 degree
Eco, Ecx - Asymmetric
Profile Horn, Linear Taper,
Axial corrugated Horn - CHAMP
Spherical Wave Expansion Coefficients
GRASP PO/PO

## Slide 33
ANTENNA BEAM AT 2.4 GHz
Θsub=15º
51.67 dB
Xpol -32.7 dB
Θsub=18º
51.73 dB
Xpol -33.5 dB
Θsub=46º
51.16 dB
Xpol -25.4 dB
Θsub=15º
52.04 dB
Xpol -37 dB
Eco, Ecx -Symmetric
Eco, Ecx - 45 degree
Eco, Ecx - Asymmetric

## Slide 34
ηa OF 18-M GREGORIAN ANTENNA
Profile Horn, Linear Taper, Axial corrugated Horn - CHAMP
Spherical Wave Expansion Coefficients
GRASP PO/PO
Chart: ha : L-BAND
| 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4
15 Pro | 60.4957 | 61.0815 | 64.294 | 67.0045 | 67.3173 | 68.1395 | 68.5933 | 68.7606 | 70.2662 | 71.3671 | 72.3438 | 72.096 | 71.7603
18 Pro | 59.5531 | 60.3851 | 62.8247 | 65.517 | 67.558 | 68.0642 | 68.8465 | 68.5961 | 69.1794 | 69.5614 | 70.1506 | 71.7482 | 72.7268
46Axial | 63.2272 | 64.4629 | 65.1689 | 66.1263 | 66.6541 | 67.2464 | 67.5945 | 68.6641 | 69.5019 | 67.6843 | 65.8994 | 64.6667 | 63.6904
15 Lin | 73.5062 | 74.4338 | 74.6226 | 74.9781 | 75.0994 | 77.5977 | 78.0444 | 77.5942 | 78.2973 | 78.1013 | 78.4172 | 78.5256 | 78.0107
ΔEff = 11%

## Slide 35
12.6-21.0 GHz FEED HORNS FOR θsub = 15º, 46º
Dia=58mm (2.4λ)
Length=20mm (0.9λ)
Θf=45⁰
# corrg. 8
Dia=203mm (8.5λ)
Length=286mm (12λ)
Θf=17.8⁰
# corrg. 88
15º
46º

## Slide 36
HALF BEAM WIDTH AT -15dB FOR θsub = 15º, 46º
15º
46º

## Slide 37
ANTENNA BEAM AT 12.5 GHz; θsub = 15º, 46º
Eco, Ecx -Symmetric
Eco, Ecx - 45 degree
Eco, Ecx - Asymmetric
Θsub=15º
66.11 dB
Xpol -40.8 dB
Θsub=46º
65.75 dB
Xpol -42.5 dB

## Slide 38
ANTENNA BEAM AT 20.5 GHz; θsub = 15º, 46º
Θsub=15º
70.64 dB
Xpol -39 dB
Θsub=46º
70.16 dB
Xpol -30.6 dB

## Slide 39
ha ANTENNA BEAM AT 21.5GHz; θsub = 15º, 46º
Θsub=15º
71.06 dB
Xpol -45 dB
Θsub=46º
70.45 dB
Xpol -28.8 dB

## Slide 40
ha 12.6-21.0 GHz FOR θsub = 15º, 46º
Linear Taper Horn, Axial corrugated Horn - CHAMP
Spherical Wave Expansion Coefficients
GRASP PO/PO
Chart: ha : Ku-Band
| 12.5 | 13.5 | 14.5 | 15.5 | 16.5 | 17.5 | 18.5 | 19.5 | 20.5 | 21.5
15Lin | 73.4745 | 74.1275 | 74.6897 | 74.902 | 73.3937 | 74.2781 | 76.8959 | 77.6171 | 77.5513 | 77.5478
46Axial | 67.5813 | 68.1725 | 68.7513 | 69.3543 | 69.5999 | 69.7237 | 70.4552 | 71.4657 | 69.3983 | 67.4139
15º
46º
ΔEff = 13%
ΔEff = 8%

## Slide 41
ha 12.6-21.0 GHz FOR θsub = 15º, 46º (21.5 GHz)

## Slide 42
CONICAL CORRUGATED HORNS

## Slide 43
APERTURE PHASE ERROR FACTOR
Δtan
r - radius at aperture
λ- wavelength
θ0- taper angle of the feed horn
Aperture phase error factor

## Slide 44
LINEAR TAPER HORN (12-18 GHz)
MEASFEED>GBTKuWide>Feed>GBTKuJULY262012>Feed patterns>summary2

## Slide 45
4. SLIDE 24 EXCESS SPILLOVER?