## Slide 1: Applications of Matched Filtering for Improved Interferometric Imaging and Weak Line Detection
Collaborators: K. Öberg, S. Andrews, C. Walsh, I. Czekala, J. Huang
Ryan A. Loomis (Harvard-Smithsonian CfA)

## Slide 2
Improvements with new interferometers

## Slide 3
  Spatial resolution
Improvements with new interferometers

## Slide 4
  Spatial resolution
  Sensitivity
Improvements with new interferometers

## Slide 5
  Spatial resolution
  Sensitivity
Improvements with new interferometers
ALMA + (2015)
TW Hya

## Slide 6
  Spatial resolution
  Sensitivity
Improvements with new interferometers
ALMA + (2015)
TW Hya
Andrews + (2016)

## Slide 7
  Spatial resolution
  Sensitivity
  Bandwidth
Improvements with new interferometers
ALMA + (2015)
TW Hya
Andrews + (2016)

## Slide 8
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Improvements with new interferometers
ALMA + (2015)
TW Hya
Andrews + (2016)

## Slide 9
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Improvements with new interferometers
ALMA + (2015)
TW Hya

## Slide 10
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Improvements with new interferometers
ALMA + (2015)
TW Hya
Jorgensen + (2016)

## Slide 11
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Point source assumptions
ALMA + (2015)
TW Hya

## Slide 12
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Point source assumptions
ALMA + (2015)
TW Hya

## Slide 13
  Spatial resolution
  Sensitivity
  Bandwidth
  Spectral resolution
Opportunities for improved techniques
ALMA + (2015)
TW Hya

## Slide 14
  Matched filtering for improved weak spectral line detection
  Generalized Briggs weighting for improved image fidelity
Outline

## Slide 15
Analyzing imaged observations
Image Cube
Channel Map
[Loomis + 2018]

## Slide 16
Analyzing imaged observations
Image Cube
Moment Maps
Channel Map
[Loomis + 2018]

## Slide 17
Analyzing imaged observations
Image Cube
Moment Maps
Channel Map
[Loomis + 2018]

## Slide 18
Analyzing imaged observations
Image Cube
Moment Maps
Channel Map
Spectra
Pixel extracted
[Loomis + 2018]

## Slide 19
Analyzing imaged observations
Image Cube
Moment Maps
Channel Map
Spectra
Pixel extracted
Aperture extracted
[Loomis + 2018]

## Slide 20
Analyzing imaged observations
Image Cube
Moment Maps
Channel Map
Spectra
Pixel extracted
Aperture extracted
Mask extracted
[Loomis + 2018]

## Slide 21
Spectral stacking
Matra + 2015
Marino + 2016
Yen + 2016

## Slide 22
https://losc.ligo.org/tutorial_optimal/
http://www.grauonline.de/alexwww/ardumower/filter/filter.html
Convolve known template signal with noisy data
Signal (used as filter/kernel)
Noisy signal
Matched filtering

## Slide 23
https://losc.ligo.org/tutorial_optimal/
http://www.grauonline.de/alexwww/ardumower/filter/filter.html
Convolve known template signal with noisy data
Signal (used as filter/kernel)
Noisy signal
Matched filtering

## Slide 24
https://losc.ligo.org/tutorial_optimal/
http://www.grauonline.de/alexwww/ardumower/filter/filter.html
Convolve known template signal with noisy data
Signal (used as filter/kernel)
Autocorrelation of signal
Noisy signal
Filter response
Filter response has highest recoverable SNR
Matched filtering

## Slide 25
Matched filtering interferometric data
KERNEL (f)
DATA (V)
nk
nuv
nc
FFT
nuv
[Loomis + 2018]

## Slide 26
Matched filtering interferometric data
*
KERNEL (f)
DATA (V)
nk
nuv
nc
FFT
[Loomis + 2018]

## Slide 27
Matched filtering interferometric data
*
KERNEL (f)
DATA (V)
nk
nuv
IMPULSE RESPONSE SPECTRUM (T)
nc
FFT
[Loomis + 2018]

## Slide 28
Matched filtering interferometric data
*
KERNEL (f)
DATA (V)
nk
nuv
IMPULSE RESPONSE SPECTRUM (T)
nc
FFT
[Loomis + 2018]

## Slide 29
Matched filtering interferometric data
*
KERNEL (f)
DATA (V)
nk
nuv
IMPULSE RESPONSE SPECTRUM (T)
nc
*
FFT
[Loomis + 2018]

## Slide 30
Matched filtering interferometric data
*
KERNEL (f)
DATA (V)
nk
nuv
IMPULSE RESPONSE SPECTRUM (T)
nc
*
*
FFT
[Loomis + 2018]

## Slide 31
[Walsh, Loomis, Öberg + 2016]
Test case #1 – CH3OH in TW Hya

## Slide 32
[Loomis + 2018]
Test case #1 – CH3OH in TW Hya

## Slide 33
Individual lines are now detected
SNR significantly enhanced – 7.8σ after matched filtering vs 5.1σ before (53% improvement)
53% SNR boost is equivalent to a factor of 2.3 in observing time
Test case #1 – CH3OH in TW Hya
[Loomis + 2018]

## Slide 34
H2CO 303-202
Test case #2 – H2CO in HD 163296
Carney + 2017

## Slide 35
H2CO 322-221 + 321-220 Stacked Spectra
Test case #2 – H2CO in HD 163296
Carney + 2017
322-221 + 321-220 Moment-0

## Slide 36
Matched filter
>500% SNR boost!
H2CO 322-221 + 321-220 Stacked Spectra
Test case #2 – H2CO in HD 163296
Carney + 2017
322-221 + 321-220 Moment-0

## Slide 37
Matched filter
>500% SNR boost!
H2CO 322-221 + 321-220 Stacked Spectra
Test case #2 – H2CO in HD 163296
Carney + 2017
H2CO Response Spectra

## Slide 38
ALMA Band 7 Disk Spectral Survey
Aperture-extraction
~40-50 hrs to image, clean, and extract spectra
10 detected species
[Loomis + in prep]

## Slide 39
ALMA Band 7 Disk Spectral Survey
Aperture-extraction
~40-50 hrs to image, clean, and extract spectra
10 detected species
Matched filtering
~30 min to filter entire survey
SNR 2-3x higher
16 detected species
5 new disk species: 13CS, C34S, DNC, CCD, H2CS
[Loomis + in prep]

## Slide 40
Matched filtering can boost SNR of weak spectral lines by >500%
Useful for fast uv plane analysis of large bandwidth datasets
  No prior imaging necessary!
Not limited to disks – method is general
  Ideal for resolved sources with PV structure
Summary

## Slide 41
  Matched filtering for improved weak spectral line detection
  Generalized Briggs weighting for improved image fidelity
Outline

## Slide 42
Many resolved sources now showing sub-structure
SNR limitations may prevent imaging this sub-structure in weaker sources
Ansdell + 2016
Motivation
Notes: ----- Meeting Notes (10/6/16 14:59) -----
maybe even explicitly mention brigg's thesis chapter 3.5.2 (e.g.)

## Slide 43
Natural – lowest rms in dirty image
Uniform – lowest sidelobes, higher resolution
Robust – tunable between natural and uniform
  Retains benefits of both
Tapering – generally Gaussian taper
  Sacrifices resolution for increased sensitivity to extended structure
Types of weighting

## Slide 44
Briggs 1995
Robust weighting

## Slide 45
Briggs 1995
UV coverage and array balance

## Slide 46
Briggs 1995
Robust weighting

## Slide 47
Eric Murphy’s bulletin board
UV coverage and array balance
ALMA
ngVLA

## Slide 48
Why does robust weighting work?

## Slide 49
Weights:
Briggs 1995
Definitions

## Slide 50
Weights:
Taper weights
Briggs 1995
Definitions

## Slide 51
Weights:
Taper weights
Density weights
Briggs 1995
Definitions

## Slide 52
Weights:
Taper weights
Density weights
SNR weights = 1/σk2
Briggs 1995
Definitions

## Slide 53
Dirty image:
Weights:
Taper weights
Density weights
SNR weights = 1/σk2
Briggs 1995
Definitions

## Slide 54
Dirty image:
Weights:
Taper weights
Density weights
Variance of the dirty image:
SNR weights = 1/σk2
Briggs 1995
Definitions

## Slide 55
Dirty image:
Weights:
Taper weights
Density weights
Variance of the dirty image:
RMS thermal noise:
SNR weights = 1/σk2
Briggs 1995
Definitions

## Slide 56
Minimize (ΔID)2 using Lagrangian multiplier:
Briggs 1995
Natural weighting

## Slide 57
Minimize (ΔID)2 using Lagrangian multiplier:
Thermal noise is lowest if Tk and Dk = 1, as wk = 1/σk2
Briggs 1995
Natural weighting

## Slide 58
Minimize sidelobes by minimizing beam power ||B||2:
Briggs 1995
Uniform weighting

## Slide 59
Minimize sidelobes by minimizing beam power ||B||2:
Briggs 1995
Uniform weighting

## Slide 60
Minimize sidelobes by minimizing beam power ||B||2:
Briggs 1995
Uniform weighting

## Slide 61
Find a smooth knob between natural and uniform weighting through minimization
Briggs 1995
Robust weighting

## Slide 62
Natural weighting is only ideal for a point source
Briggs 1995
‘Natural’ weighting for a resolved source

## Slide 63
Natural weighting is only ideal for a point source
Maximize SNR for an arbitrary source: V
Briggs 1995
‘Natural’ weighting for a resolved source
SNR:

## Slide 64
Natural weighting is only ideal for a point source
TkDkwk 1/σk2 becomes: TkDkwk Re(Vk)/σk2
Maximize SNR for an arbitrary source: V
Briggs 1995
‘Natural’ weighting for a resolved source
SNR:

## Slide 65
Natural weighting is only ideal for a point source
TkDkwk 1/σk2 becomes: TkDkwk Re(Vk)/σk2
Gaussian tapering increases SNR of resolved sources because the taper approximates a matched filter
Maximize SNR for an arbitrary source: V
TkDkwk |Vk|/σk2
Briggs 1995
‘Natural’ weighting for a resolved source
SNR:

## Slide 66
Can we find a way to connect matched filter weighting with uniform weighting?
Generalized Briggs robust weighting

## Slide 67
Can we find a way to connect matched filter weighting with uniform weighting?
Minimize:
Generalized Briggs robust weighting

## Slide 68
Can we find a way to connect matched filter weighting with uniform weighting?
Minimize:
Find that:
Generalized Briggs robust weighting

## Slide 69
Robust
Gaussian taper
Generalized robust
Test case - ring

## Slide 70
Test case - ring
Robust weighting
Gaussian taper
Generalized robust

## Slide 71
Robust
Gaussian taper
Generalized robust
Realistic example – AA Tau

## Slide 72
SNR = 49
SNR = 87
Uniform weighting
Generalized Briggs
Realistic example – AA Tau
Loomis + 2017

## Slide 73
Generalized robust weighting outperforms robust weighting for all extended sources, and reduces to robust weighting for point sources
Especially shines in comparison to tapering, good for cases where you need a little extra SNR, but want to preserve resolution
Need knowledge of source structure – CLEAN model is an estimate of this!
Summary

## Slide 74
Matched filtering allows priors to be leveraged, increasing spectral SNR and image fidelity
Prior constraints can be derived from the data itself, or from astrophysical/chemical models
VISIBLE tool available for use! Check it out at: github.com/AstroChem/VISIBLE
Generalized robust weighting implemented in CASA, stay tuned for release
Summary

## Slide 75
SNR boost is proportional to resolution

## Slide 76: Kernel generation

## Slide 77: vis_sample
Python implementation of uvmodelhttps://github.com/AstroChem/vis_sample
~25% faster than uvmodel
Accepts FITS cubes (i.e. from LIME) and RADMC-3D output files
Interfaces with CASA measurement sets (input and output)

## Slide 78
  Kernel interpolation
  Streamlined loading of data
  Automated line identification
  Response normalization
  Response spectra regridding and averaging
  Screening against catalogues
Development for survey implementation

## Slide 79
  MWC 480 – 12 species (13C18O, N2H+, DCN, DCO+, CH3CN, HC3N, C2D, c-C3H2, H2CO, H2CN, H2CS, CS)
  LkCa 15 – 10 species (13C18O, N2H+, DCN, DCO+, DNC, c-C3H2, H2CO, H2CN, CS, C34S)
Disk Spectral Survey