## Slide 1: A Crash Course in Radio Astronomy and Interferometry: 1. Basic Radio/mm Astronomy
James Di Francesco
National Research Council of Canada
North American ALMA Regional Center – Victoria
(thanks to S. Dougherty, C. Chandler, D. Wilner & C. Brogan)

## Slide 2: Intensity & Flux Density
EM power in bandwidth dn from solid angle dW intercepted by surface dA is:
Defines surface brightness Iv (W m-2 Hz-1 sr-1 ; aka specific intensity)
Note:
Flux density Sv (W m-2 Hz-1) – integrate brightness over solid angle of source
Convenient unit – the Jansky  1 Jy = 10-26 W m-2 Hz-1 = 10-23 erg s-1 cm-2 Hz-1
Basic Radio/mm Astronomy

## Slide 3
In general surface brightness is position dependent, ie. In = In(q,f)
(if In described by a blackbody in the Rayleigh-Jeans limit; hn/kT << 1)
Back to flux:
In general, a radio telescope maps the temperature distribution of the sky
Basic Radio/mm Astronomy
Surface Brightness

## Slide 4: Brightness Temperature
Many astronomical sources DO NOT emit as blackbodies!
However….
Brightness temperature (TB) of a source is defined as the temperature of a blackbody with the same surface brightness at a given frequency:
This implies that the flux density
Basic Radio Astronomy

## Slide 5
Recall :
Telescope of effective area Ae receives power Prec per unit frequency from an unpolarized source but is only sensitive to one mode of polarization:
Telescope is sensitive to radiation from more than one direction with relative sensitivity given by the normalized antenna pattern PN(q,j):
Basic Radio Astronomy
What does a Radio Telescope Detect?

## Slide 6
Johnson-Nyquist theorem (1928):
Antenna temperature is what is observed by the radio telescope.
Power received by the antenna:
A “convolution” of sky brightness with the beam pattern
It is an inversion problem to determine the source temperature distribution.
Basic Radio Astronomy
Antenna Temperature

## Slide 7
The antenna collects the E-field over the aperture at the focus
The feed horn at the focus adds the fields together, guides signal to the front end
Basic Radio/mm Astronomy
Radio Telescopes

## Slide 8
Amplifier
  amplifies a very weak radio frequency (RF) signal, is stable & low noise
Mixer
  produces a stable lower, intermediate frequency (IF) signal by mixing the RF signal with a stable local oscillator (LO) signal, is tunable
Filter – selects a narrow signal band out of the IF
Backend – either total power detector or more typically today, a correlator
Basic Radio/mm Astronomy
Components of a Heterodyne System
Back end
Power detector/integrator
or Correlator
Feed Horn

## Slide 9
Antenna response is a coherent phase summation of the E-field at the focus
First null occurs at the angle where one extra wavelength of path is added across the full aperture width,
i.e., q ~ l/D
On-axis
incidence
Off-axis
incidence
Basic Radio/mm Astronomy
Origin of the Beam Pattern

## Slide 10
Defines telescope resolution
Basic Radio/mm Astronomy
Antenna Power Pattern
The voltage response pattern is the FT of the aperture distribution
The power response pattern, P(q ) µ V2(q ), is the FT of the autocorrelation function of the aperture
for a uniform circle, V(q ) is J1(x)/x and P(q ) is the Airy pattern, (J1(x)/x)2

## Slide 11
The antenna “beam” solid
angle on the sky is:
Sidelobes
NB: rear lobes!
Basic Radio/mm Astronomy
The Beam
q (“)
D (m)
0.35
508
SMA
4.5
50
LMT
15
15
JCMT
103
1.7
AST/RO
0.012
15 000
ALMA
Telescope beams @ 345 GHz

## Slide 12
Unfortunately, the telescope system itself contributes noise to the the signal detected by the telescope, i.e.,
Pout = PA + Psys  Tout = TA + Tsys
The system temperature, Tsys, represents noise added by the system:
Tsys = Tbg + Tsky + Tspill + Tloss + Tcal + Trx
Tbg = microwave and galactic background (3K, except below 1GHz)
Tsky = atmospheric emission (increases with frequency--dominant in mm)
Tspill = ground radiation (via sidelobes) (telescope design)
Tloss = losses in the feed and signal transmission system (design)
Tcal = injected calibrator signal (usually small)
Trx = receiver system (often dominates at cm — a design challenge)
Note that Tbg, Tsky, and Tspill vary with sky position and Tsky is time variable
Basic Radio/mm Astronomy
Sensitivity (Noise)

## Slide 13
In the mm/submm regime, Tsky is the challenge (especially at low elevations)
In general, Trx is essentially at the quantum limit, and Trx < Tsky
< 175
602-720
Band 9
< 83
275-370
Band 7
< 83
211-275
Band 6
< 37
84-116
Band 3
Trx (K)
GHz
ALMA Trx
Basic Radio/mm Astronomy
Sensitivity (Noise)
“Dry” component: O2
“Wet” component: H2O

## Slide 14
Q: How can you detect TA (signal) in the presence of Tsys (noise)?
A: The signal is correlated from one sample to the next but the noise is not
For bandwidth Dn, samples taken less than Dt = 1/Dn are not independent
(Nyquist sampling theorem!)
Time t contains independent samples
Radiometer equation
For Gaussian noise, total error for N samples is
that of single sample
Basic Radio/mm Astronomy
Sensitivity (Noise)

## Slide 15: Next: Aperture Synthesis